## Slide 1
AI + IOT DATASHEET
REV 2.0
UNIHIKER
K10
AI + IOT DEVELOPMENT BOARD
A pocket-sized, touchscreen coding board that brings computer vision, voice AI, TinyML and IoT together in one classroom-ready device.
VISION
VOICE
WIFI/BT
TINYML
01 / 10

## Slide 2
OVERVIEW
What Is the UNIHIKER K10?
The UNIHIKER K10 is an all-in-one educational development board that lets students learn AI, IoT, and coding using a single device — no breadboards, no extra wiring, no extra parts. A 2MP camera, dual microphones, a speaker, a 2.8" color touchscreen, and a full environmental sensor suite are built straight onto the board, so learners go from unboxing to their first AI project in minutes.
TYPE
All-in-one educational AI + IoT board
SUPPORTS
AI · IoT · Python · Block Coding
BUILT FOR
Students, teachers, and STEM makers
ONBOARD I/O
Touchscreen · Camera + Mic · Sensors
K10
TOUCHSCREEN
CAMERA + MIC
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
02 / 10

## Slide 3
SPECIFICATIONS
Full Technical Specifications
PROCESSOR
ESP32-S3 (Xtensa LX7), dual-core
MEMORY
512 KB SRAM
STORAGE
16 MB onboard flash + microSD slot
DISPLAY
2.8" color touchscreen, 240 × 320
CAMERA
2 MP onboard vision sensor
AUDIO
2-mic array, onboard speaker
WIRELESS
Wi-Fi 2.4G + Bluetooth 5.0
POWER INPUT
3.5–5.5V DC via USB-C or DC2.1
PORTS
USB-C, Gravity 3/4-pin, edge connector
EXPANSION
microSD + Gravity sensor/actuator I/O
DIMENSIONS
250 × 190 × 57 mm (packaged)
WEIGHT
647 g (packaged)
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
03 / 10

## Slide 4
HARDWARE
Main Features
Camera
2MP vision sensor for AI recognition
Mic & Speaker
2-mic array plus onboard audio out
Color Display
2.8" touchscreen for live feedback
Wi-Fi & Bluetooth
Dual wireless for IoT & remote control
Built-in Sensors
Temp, humidity, light & motion onboard
Expansion Ports
Gravity + edge connector for add-ons
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
04 / 10

## Slide 5
SENSORS & I/O
Built-In Sensors & Expansion Ports
SENSOR SUITE
Ambient light sensor
Humidity sensor
Temperature sensor
Motion / gyroscope
2MP camera (vision AI)
Dual microphone array
PORTS & EXPANSION
USB Type-C
Power + programming
Gravity 3-pin / 4-pin
Sensors & actuators (PH2.0)
Edge connector
Direct board-to-board mounting
microSD slot
Local data logging & storage
2-pin battery port
Portable, untethered projects
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
05 / 10

## Slide 6
CAPABILITIES
What You Can Do With It
01
Learn Coding
Block coding in Mind+ or MicroPython
02
AI Projects
Face, object & pet detection with TinyML
03
IoT Projects
Send sensor data over Wi-Fi/Bluetooth
04
Robotics
Drive motors & actuators via Gravity I/O
05
Smart Devices
Build touchscreen smart-home controllers
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
06 / 10

## Slide 7
APPLICATIONS
Real-World Applications
Face Recognition
Unlock, greet, or personalize with on-device detection
Voice Assistant
Offline speech recognition & custom voice commands
Weather Station
Log temperature, humidity & light over time
Smart Home
Trigger lights, fans & alerts from sensor data
Attendance System
QR/badge scanning for classroom check-in
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
07 / 10

## Slide 8
TOOLCHAIN
How You Program It
Mind+
Visual, block-based coding for total beginners
drag & drop blocks
MicroPython
Full Python scripting for AI & sensor logic
$ python main.py
Arduino IDE
Familiar C/C++ workflow for makers
$ arduino-cli upload
PlatformIO
Pro-grade builds, debugging & CI
$ pio run --upload
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
08 / 10

## Slide 9
GETTING STARTED
What's In The Box & Quick Start
PACKAGE CONTENTS
1 × UNIHIKER K10 board
1 × USB Type-C cable
Quick-start guide card
Access to online wiki & courses
Available now
via DFRobot & authorized education resellers
3-STEP QUICK START
01
Plug in
Connect the K10 to your computer with the included USB-C cable
02
Install Mind+
Download the free Mind+ app and connect to your board
03
Drag & run
Drag your first AI block onto the canvas and hit run
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
09 / 10

## Slide 10
FINAL — SUMMARY
One Board. Every Skill.
UNIHIKER K10 helps students learn AI, coding, electronics, and IoT through practical, hands-on projects — combining vision, voice, connectivity and TinyML into one board built for the classroom.
VISION
VOICE
WIFI/BT
TINYML
UNIHIKER K10 · AI + IoT DATASHEET · REV 2.0
10 / 10